## Slide 1: SDN & NFV Lab 1: ONOS/Ryu + Mininet
Environment Setup & Basic Operation
Date: | 2019/02/18 (Mon.) 9:00
Deadline: | 2019/02/24 (Mon.) 23:59

## Slide 2: Overview
Mininet
ONOS
Virtual Machine
Use ONOS GUI to
see the topology
switch
host
host

## Slide 3: Outline
Environment Setup
  VirtualBox Installation
  Ryu Installation
  ONOS Installation
  Mininet Installation
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
    [Way 1] Mininet CLI: “--topo” option
    [Way 2] Custom Topology: Python script
Project1 requirements

## Slide 4: Outline
Environment Setup
  VirtualBox Installation
  Ryu Installation
  ONOS Installation
  Mininet Installation
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
Project1 requirements

## Slide 5: Environment Setup
VirtualBox & ONOS & Mininet

## Slide 6: Outline
Environment Setup
  VirtualBox Installation
  Ryu Installation
  ONOS Installation
  Mininet Installation
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
Project1 requirements

## Slide 7: Prepare a Operational Environment
VirtualBox: Open source cross-platform virtualization application
  Use Ubuntu 16.04
  Recommended Hardware requirement
    2 Cores
    4G RAM
    40G HDD
For more information, please refers to:
  [File] SDN_Environment_Setup.pptx

## Slide 8: Outline
Environment Setup
  VirtualBox Installation
  Ryu Installation
  ONOS Installation
  Mininet Installation
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
Project1 requirements

## Slide 9: Ryu Installation
Install dependencies
Install Ryu from source code
For more information, please refer to:
  Github
  Ryu Document
  Ryubook 1.0 (For your reference of future work on applications)
$ sudo apt install gcc python-dev libffi-dev libssl-dev libxml2-dev libxslt1-dev zlib1g-dev
$ git clone git://github.com/osrg/ryu.git
$ cd ryu; pip install .

## Slide 10: Outline
Environment Setup
  VirtualBox Installation
  Ryu Installation
  ONOS Installation
    ONOS Dependencies Installation
    Bazel Installation
    ONOS Installation
  Mininet Installation
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
Project1 requirements

## Slide 11: ONOS Dependencies Installation
Java dependency
Other dependencies
$ sudo apt-get install software-properties-common -y && \
sudo add-apt-repository ppa:webupd8team/java -y && \
sudo apt-get update && \
echo "oracle-java8-installer shared/accepted-oracle-license-v1-1 select true" | sudo debconf-set-selections && \
sudo apt-get install oracle-java8-installer oracle-java8-set-default -y
$ sudo apt-get install git zip curl unzip python

## Slide 12: Bazel Installation
Install required packages
Download Bazel
Run the installer
  “--user”: Make Bazel executable installed in $HOME/bin directory.
Add $HOME/bin in default paths in ~/.bashrc file
$ sudo apt-get install pkg-config zip g++ zlib1g-dev unzip python
$ wget -c https://github.com/bazelbuild/bazel/releases/download/0.22.0/bazel-0.22.0-installer-linux-x86_64.sh
$ chmod +x bazel-0.22.0-installer-linux-x86_64.sh
$ ./bazel-0.22.0-installer-linux-x86_64.sh --user
export PATH="$PATH:$HOME/bin"

## Slide 13: ONOS Installation
Download ONOS code & checkout to version 1.15.
Build ONOS
Run ONOS.
Stop ONOS
For more information, please refer to:
  Installing Bazel on Ubuntu
  Developer Quick Start
$ cd ~/ && git clone https://gerrit.onosproject.org/onos
$ cd onos && git checkout onos-1.15
$ bazel run onos-local -- clean debug
<ctl + C>
$ bazel build onos
Notes: Clean debug 作用

## Slide 14: Outline
Environment Setup
  VirtualBox Installation
  Ryu Installation
  ONOS Installation
  Mininet Installation
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
Project1 requirements

## Slide 15: Mininet Installation
Download from source code & build Mininet
Exit mininet shell
Clean the environment
$ cd ~/ && git clone https://github.com/mininet/mininet
$ cd mininet
$ util/install.sh -a
$ sudo mn -c
mininet> exit

## Slide 16: Outline
Environment Setup
  VirtualBox Installation
  Ryu Installation
  ONOS Installation
  Mininet Installation
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
Project1 requirements

## Slide 17: Basic Operation
ONOS APPs & Custom Topology

## Slide 18: Outline
Environment Setup
  VirtualBox Installation
  Ryu Installation
  ONOS Installation
  Mininet Installation
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
Project1 requirements

## Slide 19: Activate basic Ryu APPs
Run Ryu controller and applications
In this project, we are going to use a repository named ryu-starter-kit provided by SDN Hub.
  https://bitbucket.org/sdnhub/ryu-starter-kit
The repository contains applications included learning switch function, web server and so on.
Follow the installation instructions, and simple run the script
$ ryu-manager yourapp.py
$ ./ryu/app/sdnhub_apps/run_sdnhub_apps.sh

## Slide 20: Outline
Environment Setup
  VirtualBox Installation
  Ryu Installation
  ONOS Installation
  Mininet Installation
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
Project1 requirements

## Slide 21: Activate basic ONOS APPs
Run ONOS in localhost.
Login into ONOS CLI
Activate applications by ONOS CLI
$ bazel run onos-local -- clean debug
onos> app activate org.onosproject.openflow
onos> app activate org.onosproject.fwd
$ tools/test/bin/onos localhost

## Slide 22: Outline
Environment Setup
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
    [Way 1] Mininet CLI: “--topo” option
      Create a topology controlled by ONOS
      Topology in ONOS GUI
      Hosts in ONOS GUI
    [Way 2] Custom Topology: Python script
Project1 requirements

## Slide 23: Create a topology controlled by Ryu/ONOS
Run Mininet controlled by ONOS
  By default, a switch would have one host
$ sudo mn --topo=linear,3 --controller=remote,ip=127.0.0.1:6653
*** Creating network
*** Adding controller
*** Adding hosts:
h1 h2 h3
*** Adding switches:
s1 s2 s3
*** Adding links:
(h1, s1) (h2, s2) (h3, s3) (s2, s1) (s3, s2)
*** Configuring hosts
h1 h2 h3
*** Starting controller
c0
*** Starting 3 switches
s1 s2 s3 ...
*** Starting CLI:
mininet>
ONOS
s1
s2
s3
h1
h2
h3

## Slide 24: Topology in Ryu GUI (SDN Hub)
Visit http://localhost:8080 on your web browser
  Use IE, Edge or FireFox if Google Chrome cannot show the topology

## Slide 25: See hosts in Ryu GUI (SDN Hub)
Use “pingall” in Mininet shell
Refresh the web page if hosts were not shown in few seconds
mininet> pingall
*** Ping: testing ping reachability
h1 -> h2 h3
h2 -> h1 h3
h3 -> h1 h2
*** Results: 0% dropped (6/6 received)
There is something wrong with host probing!
Notes: https://bitbucket.org/sdnhub/ryu-starter-kit/src/7a162d81f97d080c10beb15d8653a8e0eff8a469/host_tracker_rest.py?at=master&fileviewer=file-view-default#host_tracker_rest.py-66:67

## Slide 26: Topology in ONOS GUI
Open ONOS web page
  or alternatively visit http://localhost:8181/onos/ui
  user/password: onos/rocks
Switch information
$ tools/test/bin/onos-gui localhost
s1
s2
s3
Notes: 說明MININET會預設掛HOST+圖
截圖上方不需要

## Slide 27: See hosts in ONOS GUI
Use “pingall” in Mininet shell
Type “h” in ONOS GUI to see hosts
mininet> pingall
*** Ping: testing ping reachability
h1 -> h2 h3
h2 -> h1 h3
h3 -> h1 h2
*** Results: 0% dropped (6/6 received)
Host information
s1
s2
s3
h1
h2
h3
Notes: Us pingall to
Onos detect host only when host send packets

## Slide 28: Outline
Environment Setup
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
    [Way 1] Mininet CLI: “--topo” option
    [Way 2] Custom Topology: Python script
      Customizing “mn” using “--custom” files
      Python Script
      Add new CLI command in a “--custom” file
Project1 requirements

## Slide 29: Customizing “mn” using “--custom” files
Invoke your own custom topology
  “mn” adds new features which can be invoked
  Need to define a dict in “--custom” file (sample.py) based on the option type
    dict’s key are short names passed to the appropriate option
    dict’s value are the corresponding subclasses, constructors or functions:
“topos={}” allows the file to be imported by “--topo” option
$ sudo mn --custom=sample.py --topo=mytopo
option | dict name | Key:value
--topo | topos | ‘short name’: Topo constructor
class MyTopo( Topo ):
def build( self, ...):
...
topos = { 'mytopo': MyTopo }
Add “MyTopo” class (or constructor) to the “topos” dictionary, allowing it to be used with the “--topo” option

## Slide 30: Python Script
Edit “sample.py” and run the file
$ sudo mn --custom=sample.py --topo=mytopo \
> --controller=remote,ip=127.0.0.1,port=6653
s1(switch)
h1(host)
h2(host)

## Slide 31: Add new CLI command in a “--custom” file
Define a function in your Python script
  The command function that added to CLI should have “do_” prefix
The above function adds a “mycmd” command to Mininet CLI
def mycmd( self, line ):
"mycmd is an example command to extend the Mininet CLI"
net = self.mn
output( 'mycmd invoked for', net, 'with line', line, '\n' )
CLI.do_mycmd = mycmd
$ sudo mn --custom <python_script.py> -v output
mininet> help mycmd
mycmd is an example command to extend the Mininet CLI
mininet> mycmd foo
mycmd invoked for <mininet.net.Mininet object at 0x7fd7235fb9d0> with line foo

## Slide 32: Outline
Environment Setup
  VirtualBox Installation
  Ryu Installation
  ONOS Installation
  Mininet Installation
Basic Operation
  Activate basic Ryu APPs
  Activate basic ONOS APPs
  Create a topology controlled by Ryu/ONOS
Project1 requirements
  Answer Questions
  Write a custom Topology
  Add your own CLI command

## Slide 33: Project1 requirements
ONOS APPs & Custom Topologies & Add a new command

## Slide 34: Answer Questions - Ryu
Activate Ryu APPs
  Please find all APPs activated in run_sdnhub_apps.sh.
Observe listening ports.
  Openflow defines the TCP port for connection between controller and switch. What is the number of these ports?

## Slide 35: Answer Questions - ONOS
Activate ONOS APPs
  When activating “org.onosproject.openflow”, what are the APPs also be activated?
  Which APP enables hosts to ping each other?
Observe listening ports.
  Openflow defines the TCP port for connection between controller and switch. What is the number of these ports?
  Which APP enables the TCP port be listening?

## Slide 36: Write a Custom Topology
Use the following command to execute your script:
The class name of the topology in Python script is required to be “Project1_Topo_<studentID>”
Try to write a script to build the following topology:
s1(switch)
h1(host)
h2(host)
s2(switch)
s3(switch)
s4(switch)
h3(host)
h4(host)
$ sudo mn --custom=project1_<studentID>.py \
> --topo=topology_<studentID> \
> --controller=remote,ip=127.0.0.1:6653

## Slide 37: An example: Using studentID: 0748787
You should use the following command:
Class name in script should be: Project1_Topo_0748787
Take a screenshot with switch name and hosts
$ sudo mn --custom=project1_0748787.py \
> --topo=topology_0748787 \
> --controller=remote,ip=127.0.0.1:6653
of:000…
<hostIP>
<hostIP>
of:000…
of:000…
of:000…
<hostIP>
<hostIP>

## Slide 38: Add your own CLI command
Write a command to add a host to specific switch.
The command format should be:
The host numbering should be in order
The host IP should assign in format: 10.0.0.<host_numbering>
The command should designate new host to specific switch.
mininet> <your_command> <switch_name>
s1(switch)
h1(host)
h2(host)
s2(switch)
s3(switch)
s4(switch)
h3(host)
h4(host)
h5(host)
h6(host)

## Slide 39: An example: “addHostToSwitch” command
With the above topology wrote before.
Add two more hosts to s3 and s4
mininet> addHostToSwitch s3
mininet> pingall
*** Ping: testing ping reachability
h1 -> h2 h3 h4 h5
h2 -> h1 h3 h4 h5
h3 -> h1 h2 h4 h5
h4 -> h1 h2 h3 h5
h5 -> h1 h2 h3 h4
*** Results: 0% dropped (20/20 received)
mininet> addHostToSwitch s4
mininet> pingall
*** Ping: testing ping reachability
h1 -> h2 h3 h4 h5 h6
h2 -> h1 h3 h4 h5 h6
h3 -> h1 h2 h4 h5 h6
h4 -> h1 h2 h3 h5 h6
h5 -> h1 h2 h3 h4 h6
h6 -> h1 h2 h3 h4 h5
*** Results: 0% dropped (30/30 received)
ca.nctu.edu.tw

## Slide 40: Additional Description

## Slide 41: Network Topology for Emulation
Mininet uses the root namespace, the only way to run OVS
  Observe the linear topology with two devices
    s1 has two interfaces: s1-eth1 and s1-eth2
Root namespace
eth0
Software switch
h1 namespace
h1-eth0
Process 1
h2 namespace
h2-eth0
Process 2
s1-eth1
s1-eth2
veth
s2-eth2
s2-eth1
veth
socket
socket
s1
s2
h1(host)
h2(host)
s1-eth1
s1-eth2
s2-eth1
s2-eth2

## Slide 42: Recommended Procedure
Add a switch and a host in the topology
Add a link between the switch and the host
Find the new interface of the switch
Attach the interface to the switch
Set IP for the host
Mininet API
  mininet.net.Mininet Class
  mininet.node.Node Class
  mininet.node.OVSSwitch Class

## Slide 43: Submit
Report & Python script

## Slide 44: Submit to e3
Files
  A python script: <You have to name it>.py
  A report: project1_studentID.pdf
    Record your process (especially your command)
    Take screenshots (ONOS GUI or CLI) and explain or mark them
    Write down what you learn or solve
Submit
  Upload “.zip” file to e3
    Named: project1_studentID.zip
  Wrong file name or format would not be scored
Demo
  Show your own command to add new host to specific switch.

## Slide 45: Thank you
Q & A