## Slide 1: Write a Custom Topology in Lab 1
Our assigned topology is as follow
  Which has a loop inside
The forwarding application in SDN HUB project is learning switch
  Loops could result in broadcast storm during flooding
s1(switch)
h1(host)
h2(host)
s2(switch)
s3(switch)
s4(switch)
h3(host)
h4(host)

## Slide 2: For those who use Ryu controller
With our custom topology in this lab, please open Ryu with SimpleSwitchStp13 application
STP requires about 30 seconds to learn
  Wait this period after you start Mininet, and then ping can work
Ryubook Spanning Tree
  https://osrg.github.io/ryu-book/en/html/spanning_tree.html
$ ryu-manager ryu.app.simple_switch_stp_13

## Slide 3: Project 2
OpenFlow Protocol Observation and Flow Rule Installation
Date: | 2019/02/25 (Mon.)
Deadline: | 2019/03/14 (Thu.)

## Slide 4: Outline
Observe OpenFlow Messages
  Wireshark
  On Ryu
  On ONOS
Install/Delete Flow Rules with REST
  On Ryu
  On ONOS
Project 2 requirements

## Slide 5: Outline
Observe OpenFlow Messages
  Wireshark
  On Ryu
  On ONOS
Install/Delete Flow Rules with REST
  On Ryu
  On ONOS
Project 2 requirements

## Slide 6: Observe OpenFlow Messages
OpenFlow Protocol Observation and Flow Rule Installation
Notes: 說明有兩種方式 CLI AND restful api

## Slide 7: Outline
Observe OpenFlow Messages
  Wireshark
  On Ryu
  On ONOS
Install/Delete Flow Rules with REST
  On Ryu
  On ONOS
Project 2 requirements

## Slide 8: Wireshark
A free and open-source packet analyzer
Installation (Ubuntu should have Wireshark installed)
Open Wireshark
$ sudo apt-get install wireshark
$ sudo wireshark

## Slide 9: Capture Packets
Capture packets on Loopback interface

## Slide 10: Outline
Observe OpenFlow Messages
  Wireshark
  On Ryu
  On ONOS
Install/Delete Flow Rules with REST
  On Ryu
  On ONOS
Project 2 requirements

## Slide 11: Observe OpenFlow Messages on Ryu
Start SimpleSwitch13 application on Ryu
Start Mininet topology
Start capture packets on Loopback interface with Wireshark
Ping a host in Mininet (Please ping h2 from h1 in this lab)
Stop ping and Wireshark to check captured packets
$ cd ryu
$ ryu-manager ryu.app.simple_switch_13
$ sudo mn --controller=remote,127.0.0.1:6653
mininet> h1 ping h2

## Slide 12: Outline
Observe OpenFlow Messages
  Wireshark
  On Ryu
  On ONOS
Install/Delete Flow Rules with REST
  On Ryu
  On ONOS
Project 2 requirements

## Slide 13: Observe OpenFlow Messages on ONOS
Start ONOS and check activated application on ONOS CLI
Start Mininet topology
Start capture packets on Loopback interface with Wireshark
Ping a host in Mininet (Please ping h2 from h1 in this lab)
Stop ping and Wireshark to check captured packets
onos> apps –a –s # Check activated application
onos> app activate fwd # Activate ReactiveForwarding
onos> app deactivate proxyarp # Deactivate ProxyARP
$ sudo mn --controller=remote,127.0.0.1:6653
mininet> h1 ping h2

## Slide 14: Information for Reference
Command `sudo mn` builds a topology with a switch and two hosts connected
OpenFlow spec 1.3
  https://www.opennetworking.org/wp-content/uploads/2014/10/openflow-spec-v1.3.0.pdf
Ryubook SimpleSwitch13
  https://osrg.github.io/ryu-book/en/html/switching_hub.html
s1
h2
h1

## Slide 15: Outline
Observe OpenFlow Messages
  Wireshark
  On Ryu
  On ONOS
Install/Delete Flow Rules with REST
  On Ryu
  On ONOS
Project 2 requirements

## Slide 16: Install/Delete Flow Rules with REST
OpenFlow Protocol Observation and Flow Rule Installation
Notes: 說明有兩種方式 CLI AND restful api

## Slide 17: REST (I)
Representational State Transfer (REST) is a software architectural style for creating Web services
  Client-server architecture
  Statelessness
  Cacheability
  Uniform interface
Allow to access and manipulate textual representations of Web resources
  HTTP method is used, as is the most common
  Payload could be formatted in HTML, XML, JSON

## Slide 18: REST (II)
Command `curl` is used to transfer data from or to a server
`<data>` could be a file name if prefixed with `@` character
$ curl –u <user:password> -X <command> -H <header> -d <data> [URL]
$ curl –u <user:password> -X <command> -H <header> -d @<file> [URL]

## Slide 19: Outline
Observe OpenFlow Messages
  Wireshark
  On Ryu
  On ONOS
Install/Delete Flow Rules with REST
  On Ryu
  On ONOS
Project 2 requirements

## Slide 20: Ryu Setup
Start SimpleSwitch13 application on Ryu
Start Mininet topology
Check that two hosts cannot ping each other
$ cd ryu
$ ryu-manager ryu.app.ofctl_rest
$ sudo mn --controller=remote,127.0.0.1:6653
mininet> h1 ping h2

## Slide 21: Install Flow Rules on Ryu
$ curl -X POST -d '{
"dpid": 1,
"cookie": 1,
"cookie_mask": 1,
"table_id": 0,
"idle_timeout": 30,
"hard_timeout": 30,
"priority": 11111,
"flags": 1,
"match":{
"in_port":2
},
"actions":[
{
"type":"OUTPUT",
"port": 1
}
]
}' http://localhost:8080/stats/flowentry/add

## Slide 22: Delete Flow Rules on Ryu
Delete all matching flow entries of the switch
  The fields to match depend on what kind of flows to delete
Delete all flow entries of the switch which specified with Datapath ID in URI (/stats/flowentry/clear/<dpid>)
$ curl -X DELETE http://localhost:8080/stats/flowentry/clear/1
$ curl -X POST -d '{
"dpid": 1,
"cookie": 2,
"cookie_mask": 1,
}' http://localhost:8080/stats/flowentry/delete

## Slide 23: Outline
Observe OpenFlow Messages
  Wireshark
  On Ryu
  On ONOS
Install/Delete Flow Rules with REST
  On Ryu
  On ONOS
Project 2 requirements

## Slide 24: ONOS Setup
Make sure forwarding application is deactivated
Start Mininet topology
Check that two hosts cannot ping each other
onos> apps -a -s # Check activated application
onos> app deactivate fwd # Activate ReactiveForwarding
$ sudo mn --controller=remote,127.0.0.1:6653
mininet> h1 ping h2

## Slide 25: Create a JSON file of flow rules
    {
    "priority": 40000,
    "timeout": 0,
    "isPermanent": true,
    "deviceId": "of:0000000000000001",
    "treatment": {
    "instructions": [
    {
    "type": "OUTPUT",
    "port": "2"
    }
    ]
    },
    "selector": {
    "criteria": [
    {
    "type": "IN_PORT",
    "port": "1"
    }
    ]
    }
    }
Notice that this is the content of your JSON file of flow rules, not commands on terminal!

## Slide 26: Install Flow Rules on ONOS
Install flow rules on ONOS with JSON file say `flows1.json`
$ curl -u onos:rocks -X POST -H “Content-Type: application/json” -d @flows1.json http://localhost:8181/onos/v1/flows/of:0000000000000001
Please type the command yourself.
Do not copy and paste since the quotation marks (“) could be different!

## Slide 27: Delete Flow Rules on ONOS (I)
Find flow ID of the flow rule to delete on http://localhost:8181/onos/v1/flows/of:0000000000000001
`curl` could also be used
In this example, flow ID is 51509923833076777.
$ curl -u onos:rocks -X GET -H “Accept: application/json” http://localhost:8181/onos/v1/flows/of:0000000000000001

## Slide 28: Delete Flow Rules on ONOS (II)
Delete the flow rule with flow ID
$ curl -u onos:rocks -X DELETE -H “Accept: application/json” http://localhost:8181/onos/v1/flows/of:0000000000000001/ 51509923833076777

## Slide 29: ONOS REST API on Web UI (I)
Browse http://127.0.0.1:8181/onos/v1/docs

## Slide 30: ONOS REST API on Web UI (II)
Fill out required fields (`appID` could be arbitrary string)

## Slide 31: Information for Reference
Manpages for command `curl`
  http://manpages.ubuntu.com/manpages/xenial/man1/curl.1.html
Ryu REST API application
  https://ryu.readthedocs.io/en/latest/app/ofctl_rest.html#
ONOS REST API
  https://wiki.onosproject.org/display/ONOS/Appendix+B%3A+REST+API
  Notice that the priority should be less than 65535

## Slide 32: Outline
Observe OpenFlow Messages
  Wireshark
  On Ryu
  On ONOS
Install/Delete Flow Rules with REST
  On Ryu
  On ONOS
Project 2 Requirements

## Slide 33: Project 2 Requirements
OpenFlow Protocol Observation and Flow Rule Installation
Notes: 說明有兩種方式 CLI AND restful api

## Slide 34: Answer Questions – ONOS/Ryu
How many Flow-Mod messages are installed in captured packets?
What are the matching fields and the corresponding actions in each of Flow-Mod messages?
What are the idle timeout, hard timeout and priority of all Flow-Mod messages?

## Slide 35: Install Flow Rules (I)
Install following flow rules to forward ARP packets
  Matching fields
    Ethernet frame type (ARP)
  Actions
    Output from port
Verify your installed flows
mininet> h1 arping h2

## Slide 36: Install Flow Rules (II)
Install following flow rules to forward IPv4 packets
  Matching fields
    IPv4 destination address
  Actions
    Output from port
Verify your installed flows
Notice possible timeout for previously installed flow rules
mininet> h1 ping h2

## Slide 37: Bonus (I)
Please try to figure out what happens with data and control planes from starting to ping to the first ICMP packet that two hosts are able to reach each other
  Include the mechanism why each packet in this period is generated
  Please write down each decisions made by data and control plane in details
This involves the designs of Ryu/ONOS applications
  ONOS ReactiveForwarding
    https://github.com/opennetworkinglab/onos/blob/master/apps/fwd/src/main/java/org/onosproject/fwd/ReactiveForwarding.java
  Ryu SimpleSwitch13
    https://github.com/osrg/ryu/blob/master/ryu/app/simple_switch_13.py

## Slide 38: Bonus (II)
Ryu
  You should find the first Packet-In packet from ICMP request. However, why there is no Packet-In packet from the following ICMP response?
  One Packet-In packet should theoretically trigger Packet-Out and possibly the following Flow-Mod packet. However, you should find that the number of Packet-Out is less than that of Flow-Mod. What is the mechanism and why it is implemented?

## Slide 39: Bonus (III)
ONOS
  You should find there is one Packet-In packet from ICMP request without Packet-In packet from the following ICMP response. Why?
  How does ONOS decide ports where packets should be forwarded?
Hint for ONOS: a period of lag should be predicted since the mechanism of ReactiveForwarding

## Slide 40: Submit to e3
Files
  A report: project2_studentID.pdf
    Take screenshots of your captures from Wireshark (OpenFlow messages)
    Answer the questions in details
    Record your process of installing flow rules (include JSON)
    Write down what you learn or solve
Submit
  Upload “.zip” file to e3
    Named: project2_studentID.zip
  Wrong file name or format would not be scored

## Slide 41: Thank you
Q & A